# Universal aluminium volleyball posts

Assembly manual

Volleyball posts are designed to be used indoor, as well as outdoor. However, we recommend to store the posts indoor during winter.

- Place the sleeve (2) in the ground, at angle 1-2 degrees to the outside part of the playing area, in the way that the height of the posts (1) would be 2,55m when measured from the playing field surface. Posts should be installed in the sleeves 350 mm below the playground level. Size of foundation for sleeve depends on the type of floor and should meet the following requirement: horizontal force P=2000N at height 2430mm should not cause the loosening of connection of post bindings.

- Set the height of the net (5) by adjusting in one line the level marked on posts (1) with the top edge of slider (3) – for this reason settle the sliders’ position (3) by temporarily locking the knob (10) and inserting screws (4) in adequate holes in the posts (1).

- Fasten the string of net adjustment (5) to the sliders’ hooks (3) and stretch with a stretching mechanism (6)

- Put the protection pads (7) on the posts (1). Leave a small gap enabling movement of sliders (3) in marked levels and pin the protections with belts (8).

- Height marking on the posts (1) in meters:

- volleyball: 2,43;   2,35;   2,24;   2,20

- badminton: 1,55;   1,52

- tennis: 1,07

- There is a possibility to install additional covers for the holes in the floor (11), ref.1656

ATTENTION:

- Posts are intended for playing volleyball, badminton and tennis only.

- It is not allowed to climb the posts and net or to hang on them

- Every time after the game the suspension line should be loosened.